## Slide 1:     
Minka McInerney
& Dr. Simon Tucker

## Slide 2: Climate Change
Life cycle of buildings accounts for
40% of total global energy (1)
Material Resource
In Europe
Construction accounts for
4.8 tonnes of mineral extraction per person
per annum (2)
(3)

## Slide 3: Life Cycle Analysis
Considers the environmental impacts of a material over its life time e.g. From extraction, processing, transport, utilization & eventual disposal
System Boundary:
Cradle ...........................Gate ...........................Grave .............................Cradle
INPUTS | OUTPUTS
Raw materials | Products
(Embodied) Energy | Co products
Land Use | Waste
etc | C02e emissions (GWP)
etc | etc
Building Product LCA System boundary to ISO 14044(4) contained in a typical Material Inventory
Transport?
Operation
Re-use
Recycle
Notes: <number>

## Slide 4
Embodied Energy (EE)
The total primary energy required to produce a material
i.e. MJ/Kg
Global Warming Potential (GWP)
The metric adopted by the IPCC to assess Green House Gases
i.e. KgC02e in atmosphere over 100 years
Embodied Carbon: positive GWP of material production – a function of energy generation
Sequestered Carbon: negative GWP of the Carbon stored in plant based renewable materials
Notes: Carbon dioxide, methane, nitrous oxide
The GWP index expresses the radiative forcing effect of 1 kg of a GHG relative to 1 kg of C02 over 100 years (IPCC 2007).
<number>

## Slide 5
Non- Renewable Material
  Finite: extract once
  or develop over a long period of time
  e.g. Crude oil reserves for about 40 years (5)
Renewable Material
  One Kilogram of dried timber can contain
  1.8 Kilograms of C02eq/kg stored as Carbon
  or a negative GWP -1.8 KgC02eq/kg (5)
  Sustainability depends consumption not exceeding regeneration
  Sustainable production can have benefits to the wider ecosystem
  Procure responsibly from sustainable sources
Notes: <number>

## Slide 6: Passive house standard









Notes: 
<number>

## Slide 7: Material Implications?
Compare 2007 Building Regulation with PH Fabric Standards
Unit: | Description: | 2007 TGD Max U-Value W/m2k | 2007 TGD Insulation Depth | PH Max U-Value W/m2k | PH Insulation Depth | % additional material resource
Wall | 250mm honeycomb brick with rigid polystyrene insulation | 0.27 | 100 mm | 0.12 | 300 mm | 200%
Notes: Th
<number>

## Slide 8
But what if the additional materials were renewable and stored carbon?
Would it be possible to use the energy balance concept of passive house and apply it to a GWP balance in the design between fabric & operation?

## Slide 9: Passive House Model
ground floor
first floor
north elevation
south elevation
Four bedroom detached house
TFA = 155m2
north
Notes: 
<number>

## Slide 10: Comparative Study
Examine the
external heat loss envelope
of a generic house
i.e. floor, walls, roof, windows & doors
Designed to reach the Passive House Standard
With one house specified using principally
Renewable materials and the other using
Non-renewable materials
Compare Fabric EE & GWP with operational energy over 25 years three fuel options: gas, electricity & biomass

## Slide 11: IBO Catalogue Data (6)
  Written for Designers
  130 standard Passive House construction details
  Ecologically rated
  Material Inventory including data points for density, conductivity, EE & GWP
  LCA to ISO 14040
  GWP could be negative or positive
IBO Austrian Institute for Healthy and Ecological Building: Details for passive house-a catalogue of ecologically rated constructions
Notes: The material inventory section contains tables with the density, thermal conductivity, primary embodied energy and GWP of each material. LCA data is based on ISO 14040 and EPD data is based on ISO 14025. The characterization factors selected to measure global warming are non renewable primary energy content (EE) measured in MJ and GWP100 measured in kgC02e/kg. The net C02 factor could be positive or negative i.e. the ability to sequester C02 is included in the catalogue. The LCA system boundaries adopted are cradle to gate.
Some of the IBO catalogue data could be considered quite definitive such as density and thermal conductivity. However some of the data could be considered more uncertain such as EE and GWP.
<number>

## Slide 12: Material Inventory
 |   |   |  
 |  |  | 
 |  |  | 
 |  |  | 
 |  |  | 
 |  |  | 
 |  |  | 
 |  |  | 
 |  |  | 
 |  |  | 
 |  |  | 
 |  |  | 
 |  |  | 
 |  |  | 
 |  |  | 
 |   |   |  
 |  |  | 
 |  |  | 
 |  |  | 
 |  |  | 
 |  |  | 
 |  |  | 
 |  |  | 
 |  |  | 
 |  |  | 
 |  |  | 
 |  |  | 
 |  |  | 
 |  |  | 
Notes: The study included a simplistic verification the IBO GWP data for timber: planed spruce air dried: -1.436 kg C02eq/kg. 1 kg of dried timber can contain 1.8kg of C02eq/kg (Berge 2009). In the ICE database (where SC is not considered) sawn soft wood is attributed a GWP of between 0.20-0.59 C02eq/kg (Hammond and Jones 2011). Based on a subtraction of the Berge figures from the ICE figures, softwood could have a GWP range between -1.6 and -1.21 C02eq/kg. Thus the IBO GWP factor could be considered potentially realistic depending on how the timber is grown and processed.
<number>

## Slide 13
Ground floor 0.15 W/m2K | Ground supported concrete slab insulated externally with petrochemical based insulation
External Walls 0.12 W/m2K | Honeycomb block wall insulated externally with petrochemical based insulation rendered
Roof 0.10 W/m2K | Double T beam pitched roof with non renewable insulation with concrete tiles
Floor/Wall connection | 0.012 W/mk
Wall/Roof connection | 0.002 W/mk
Windows & Doors | uPVC treble glazed (PHI Certified)
Non-renewable Fabric
Notes: This study was confined to the building fabric associated with external heat loss and heat gains only.
<number>

## Slide 14
Ground floor 0.15 W/m2K | Suspended timber floor (with concrete screed) insulated with plant based insulation
External Walls 0.12 W/m2K | Double timber T beam stud wall insulated with plant based insulation with external timber cladding
Roof 0.10 W/m2K | Double T beam pitched roof with plant based insulation with concrete tiles
Floor/Wall connection | 0.012 W/mk
Wall/Roof connection | 0.006 W/mk
Windows & Doors | Timber treble glazed (PHI Certified)
Renewable
Fabric

## Slide 15
 | NON RENEWABLE | RENEWABLE
Specific Heat Demand <15 kWh/m2/a | 11 kWh/m2a | 12 kWh/m2a
Heat Load <10 W/m2 | 8 W/m2 | 8 W/m2
PHPP Results
Orientation | South
Air tightness (N50) | 0.3
MVHR efficiency | 93%
Notes: <number>

## Slide 16: Weight Comparison
85 Tonnes

## Slide 17: Embodied Energy Comparison fabric & operational energy 25 yrs
Fuel Options:
Gas
Electricity
Biomass
fabric
fabric
Biomass
Electricity
Gas

## Slide 18: Global Warming Potential Comparison fabric & operational energy 25 yrs
fabric
Biomass
Electricity
Gas

## Slide 19: Renewable fabric implication
Total GWP Fabric | Total GWP Fuel over 25 Years of operation (TC02e ) |  | Equivalent operational (years)
-26 TC02e | Gas | 24 | 28
 | Electricity | 93 | 7.5
 | Biomass | 16 | 41
“Zero Carbon Design?”
Notes: This table explores the metric of offsetting the positive material GWP of the renewable model against the negative fuel GWP as a tool to measure potential zero carbon design e.g. the negative GWP of the renewable fabric is the equivalent of 28 years positive operational GWP if the primary fuel is gas, 7.5 years if the primary fuel is electricity and 41 years if the primary fuel is biomass.
<number>

## Slide 20: Limitations
100 year fabric Lifespan required for -GWP
Actual GWP/EE based on quality of data
Difficulties in like for like comparisons between LCA (beginning to be addressed by voluntary Environmental Product Declarations(7))
Not all material inventories think it is appropriate to count negative GWP e.g. ICE (8)
  Science not sufficiently developed
  Overall trend of deforestation
  Plant based materials not necessarily sustainable

## Slide 21: Designers Role
Potential of Carbon Sequestration in building materials should not be ignored
EE & GWP become very significant in low energy design
Low operational energy design lends itself to simple LCA such as EE & GWP i.e. easy to calculate fabric quantities in tandem with U-value calculations
Designers should become familiar with Construction material inventories & seek Environmental Product Declarations (EPD)
Design for dematerialization(3) & durability
Source renewable materials sustainably

## Slide 22
References
(1) Dixit, M.K. et al., 2010. Identification of parameters for embodied energy measurement: A literature review. Energy and Buildings, 42(8), 1238-1274.
(2) Bribian, I.Z., Capilla, A.V. & Uson, A.A., 2008. Life cycle assessment of building materials: Comparative analysis of energy and environmental impacts and evaluation of the eco-efficiency improvement potential. Building and Environment, 40(5), 837-848.
(3) Gardner, G. & Sampat, P., 1998. Worldwatch paper 144: Mind over Matter: Recasting the role of Materials in Our Lives. Available at: www.worldwatch.org/system/files/EWP144.pdf
(4) ISO, 2006. BS EN ISO 14044:2006 Environmental management -Life cycle assessment - Requirements and guidelines.
(5) Berge, B., 2009. The Ecology of Building Materials, Oxford: Elsevier.
(6) Waltjen, T. et al., 2009. IBO Austrian Institute for Healthy and Ecological Building: Details for passive house-a catalogue of ecologically rated constructions, Vienna: SpringerWienNewYork.
(7) ISO, 2010. BS EN ISO 14025: 2010 Environmental labels and declarations - Type III environmental declarations and procedures.
(8) Hammond, G. & Jones, C., 2008. Embodied energy and carbon in construction materials. Energy, 161(EN2), 87-98.
Acknowledgements
Thesis supervisor: Dr. Simon Tucker,
Graduate School of the Environment, Centre for Alternative Technology, Wales
Contact
Minka McInerney minkaarch@gmail.com